Welding note:

1, P1 for the development of the interface, not welding.

2, component identification:

Components with no positive or negative polarity: Resistance(R1~R15),Thermistor(RT1),Ceramic capacitors

(C4,C5),Monolithic capacitor(C2,C3),Crystal oscillator(Y1),Keys（S1,S2）。

Distinguishing positive and negative elements:LED(D1~D60),Battery seat(BT1),Electrolytic capacitor(C1),

Buzzer(LS1),These elements should be noted that the positive and negative poles of the circuit board are to be noted.

Other multi pin element:STC15W408AS（U1）、DS1302（U2）、S8550（Q1）、Block USB（USB1），These

elements should be noted in the same direction as the circuit board.

3,Positive welding LED, digital tube, Thermistor, and other components of the welding in the back.

4,LED has two colors, the less number of color welding in a large number of corresponding position, and the rest of the

location of a number of more than one color.

5,U2, C4, C5, Y1, BT1 must be welded before the digital tube, pay attention to the points on the digital tube.

6,The working voltage of the kit is 5V, the battery on back is only for the power down save time.

EC1515A Electronic clock button operation instructions

Power on is time display mode(Year,Date,Time,Temperature display rotation).

Key adjust LED display style:

Adjust time operation:

Clock module don’t work after power on display:

# Text boxes

Set the Hourly Chime and alarm clock operation:

Time Display

Change LED display, there are 10 models in all.

10 seconds without key press or long press MODE for 3S

Long Press MODE for 3S

Press PLUS

Press PLUSE

Close Hourly Chime

Open Hourly Chime

Year Set

Month Set

Day Set

Hour Set

Minute Set

Time Display

Press MODE

Press MODE

Press MODE

Press MODE

Press MODE

Press MODE

Set “Year”

Press PLUS

Press PLUS

Press PLUS

Press PLUS

Press PLUS

Save Setting

Set “Month”

Set “Day”

Set “Hour”

Set “Minute”

10 seconds without the key press don’t save settings

10 seconds without the key press don’t save settings

10 seconds without the key press don’t save settings

10 seconds without the key press don’t save settings

10 seconds without the key press don’t save settings

normal

Flashing

Set hourly chime star time.

10 seconds without key press or long press MODE for 3S

E.g.:When star time is 8，and end time is 22, then from 8 to 22 clock every hour will be hourly chime.

Set hourly chime end time.

Press PLUSE

Open Alarm

Close Alarm

10 seconds without key press or long press MODE for 3S

10 seconds without key press or long press MODE for 3S

10 seconds without key press or long press MODE for 3S

Press PLUS

Press PLUS

10 seconds without key press or long press MODE for 3S

Set chime bell

Set alarm bell

Set the length of alarm time(unit: minute)

E.g.:When alarm hour is 6, and alarm minute is 30, then will be alarm at 6:30 every day .

10 seconds without key press or long press MODE for 3S

10 seconds without key press or long press MODE for 3S

10 seconds without key press or long press MODE for 3S

Press PLUS

Press PLUS

Press MODE

Press MODE

Press MODE

Press MODE

Press PLUS

Press PLUS

Press PLUS

Set alarm minute

Set alarm hour

Press MODE

Press MODE

Press MODE

Press MODE