LED lights for electronic switch that supports high-power LED lights. There are one-way switches and dual two versions, single switch can control all the way LED light switch (of course, you can put together in parallel LED control), two-way switch can be set to different switching modes.

The figure on the right black plug receiver, the right red JST connector for external power supply (that is, left output interface voltage)

If you take lithium balancing head to take power, you can balance the first turn JST adapter cable (sold separately)

Custom mode: Users can change their own light control board mode, fixed mode 1, fixed mode 2, the fixed mode three options to set a use of them. Set in later introduction in.

Features:

· Three kinds of switching mode (two-way switch)

External power supply (same output voltage and external power supply input voltage). External power supply voltage range: 2.5V - 25V.

· 2-way 3A high current output, can be connected with a plurality of LED lamps, or for driving high-power LED lights needed

Single switching mode (single switch only one output interface):

Turn once every plug the receiver channel switch, output open -> Output Off -> output open ...... cycle.

Dual-switching mode:

Switching mode 1: Turn once every plug the receiver channel switch

According to the following order cycle changes:

2 outputs closed -> A Output open, B output Close -> 2 outputs are open -> 2 outputs closed loop ......

Switching mode 2: Turn once every plug the receiver channel switch

According to the following order cycle changes:

2 outputs closed -> A Output open, B output Close -> A Output closed, B output open -> 2 outputs are open -> 2 outputs closed loop ......

Switching mode 3: Turn once every plug the receiver channel switch

According to the following order cycle changes:

2 outputs closed -> A Output open, B output Close -> 2-output closed -> A Output closed, B output open -> 2-output closed -> 2 outputs are open -> 2 outputs shut down

......cycle

Instructions:

(Under the control of the premise can support) JR plug (servo plug) into your spare receiver channel, power supply 2 outputs connected to be controlled lights, pay attention to the positive and negative! DIP plug the receiver position switch or by pressing the button insert receiver position.

Switch Mode own method:

Disconnect the receiver power, hold down the small button below shrink tube do not let go, turn the power switch board will sequentially switch mode 1, switch mode 2, to switch between 3 switch mode (if the mode last set 1, now becomes a mode 2, and so on). After releasing the button switch modes namely remember, unless it is set again.