4K Sport DV

FIREFLY 6C

- SONY Mega pixels COMS Sensor

Ver 2.0

Contents

Features ：	3

OLED Status Screen	4

Button Functions	6

Menu Description:	6

Time update:	10

Battery Charging:	10

Transferring Files:	10

Accessories installation instructions(Optional):	11

## Features ：

## OLED Status Screen

Note: Please use a C10 TF Card ( when the card speed is not match,it will show“ card speed low ”）, free up its data and format it on Firefly before use.

Performance and Specifications:

|  | Photo resolution | 16M |
| --- | --- | --- |
|  | AV output format USB Port | PAL/NTSC |
|  | HDMI Output | YES |
|  | Kind of TF card supported | Class 10 |
|  | Maximum size of TF card supported | 64G |
|  | Wi-Fi | YES |
| Specifications | Camera size | 59×41×21 MM |
|  | Weight | 70g |
|  | Battery Capacity (Battery is removable) | 1600mAH |
|  | Battery life | 1.5 hours |
|  | Time to complete charging | 2-3 hours |
|  | Compressed format | H264 |
|  | Video/photo format | *.MP4 / *.JPG |
| Optical Parameter | Diaphragm | F/2.8 ，7 glasses |
|  | Angle | Horizontal 120 degree Diagonal 170 degree |
| Electric Parameter | Working Voltage | 5V |
|  | current | 800mA |
| Working Modes | Video |
|  | Photo |
|  | Time-lapse video |
|  | Time-lapse photo |
|  | 11 Burst Photo |

## Button Functions

| Name | Functions | Descriptions |
| --- | --- | --- |
| Power/Mode Button | Turn on/off camera; select modes | Press once, camera on; press for 3 seconds, camera off/ press to select photo or video mode. |
| OK Button | start/stop recording |  |
| UP Button | move upwards | Enter menu setting/move upwards |
| DOWN Button | Move downwards | Enter menu setting/move downwards |

## Menu Description:

Video resolution: select from 4K@24fps(Quicktime player required),2.5K @30fps, 1080P 60@fps,1080P@30fps and 720p@120fps,VGA@30fps。

Time-lapse video: to start/stop time-lapse video at 0.5 / 1 / 3 / 5 /10 second intervals.

Cycle recording: If cycle recording mode is selected, the video will be cut into 5-minute segments. The earliest files will be covered when the TF card is full. (This mode is suggested to be used in vehicle monitoring.)

USB Power Up Auto-record: If this function on, it will automatically start recording when connected to external power source via USB.

(This mode is suggested to be used in vehicle monitoring or aerial photographing.)

WDR (Wide Dynamic Range): WDR function is suggested to be used in cloudy/dark environment. It might cause overexposure in sunny days.

(This mode is not suggested to be used in sunny days).

Photo resolution: 16M / 8M / 5M

(16M is suggested)

Burst photo: capture 11 photos in 1 second.

Continuous photo: This option allows you to capture photos continuously every 3 / 5 / 10 /30 second.

ISO adjustment: AUTO/100/400/1600.ISO of photos can be adjusted. At night, the lower ISO you select, the better image effect you get.

(Note: please hold your camera steady when taking photos)

Sharpness adjustment: 3 options: High, Medium and Low. Low sharpness is suggested at night.

(Under recording mode, Medium level is suggested; under photographing mode, Medium level is suggested for close-shot or in dark                   environment .

Color adjustment: 2 options: standard and vivid.

(If you want post-production, standard option is suggested.)

Time stamping: this option allows you to stamp the time on the photos or videos.

TV output mode:  PAL / NTSC

USB Auto power-off: the power will be automatically turned off in 30 seconds after the USB power supply is cut.

(This function is suggested to be used in aerial photographing.)

Angle adjustment: 2 options: Large / Medium . Small angle can reduce image distortion.

(Large angle is suggested as using smaller angle will reduce image quality.)

TF card formatting: After power on, if the format of TF card does not fit the system, you will see a tip “please format card” and please use this function then.

Factory default settings: you can use this function to resume all factory default settings.

(Note: if the camera does not work normally, please resume all factory default settings and then restart it again.)

50HZ/60HZ Light frequency setting。

ON/OFF。Turn ON to reduce Fish eye effect。

Exposure adjust：High/Middle/Low. Exposure value adjust，Lower exposure value makes more detail，but the image will darker.

Bit Rate adjust：High/Low. Higher date rate makes more detail, but the video file will bigger。

Metering way adjust：Average/Center/Spot。

System version: enter to see the system version of the camera.

## Time update:

First,delete all the files and folders in the card, and then put a “time.txt” file into the card, power up and the machine’s time will be updated .

## Battery Charging:

Connect the camera to a computer or phone charger using the included USB cable. Use 1A charger, and turn off the camera when charging will increase the charging rate. The Charging Status Light it will turn OFF when the battery is fully charged.

## Transferring Files:

1. Connect the camera to a computer via the included USB cable, and then turn on the camera.

2. Double click “My Computer” and locate “Removable Disk”. Enter “Removable Disk” and you will find all photo and video files in DV folder.

# Text boxes

1

2

3

4

5

6

7

8

9

10

11

7. USB/AV Port

8. Down Button

9. Up Button

10. TF Card Slot

11. Battery Door

- OK Button

- Camera Status LED

- OLED Status Screen

- Power/Mode Button

5. Working/Charging Status Light

6. HDMI Port

1

3

- Modes: Video/Photo

- Date

- Resolution

2

6

4

5

- Counter

- WDR Status

- FOV Level

- Battery Status。

7