programme card Appearance description

1：Low Voltage Cut-Off: The function is mainly to prevent the lithium battery pack from over discharging. When using lithium battery pack, please set the suitable value for low-voltage protection as your like. WARNING: Never use the default value “Non-protection” for lithium battery! 3.1V、2.8V、3.3V、Non-Protection

（default value 3.1V）。

2：3 start modes (Also called “Punch”) from “soft” to “very aggressive” （default value Medium）

3：Maximum brake force: （25A、45A、60A）50%，25%，75%，100%（default value 50%），（80A、120A）25%，50%，75%，100%（default value 25%）。

4：Maximum reverse force: 25%，50%，75%，100%（default value 25%）

5：Neutral range: 9%(narrow)，6%(Normal)，12%(Wide) （default value 9%）

programme card  Method：

1. Connect BEC wires with the programmer then turn on the ESC.（80A、120A  press the keys to be not  put）

2. The Green LED flashes for 2 times then LED off, that is, the connecting programmer with ESC is successful, and the Red LED on presents the current value of that item. Otherwise, the connecting is failed.

3. Please press the Key “↓” to select different programs

4. Please press the Key “→” to select different value of the current program

5. Please press the Key “Program” to confirm above selections, the Green LED on immediately and has gone out within 5 seconds, that is, this process is successful.

6. Please press the Key “Reset” to reset the factory setting.

# Text boxes

BEC interface

Low Voltage cut-off

start modes

Max brake force

Max reverse force

Neutral range

Down key

Restore factory settings key

Right key

Program key

green LED working condition