# SEC KEYPAD ALARM

MODEL: YL-353

105 dB

POSITION: CHIME; INSTANT; DELAY

BATTERY: 3 AA SIZE (4.5V)

INSTRUCTION (YL-353)

- WHAT’S THE FUNCTION

The magnetic sensor can detect the opening of doors or windows and give out a signal to the main unit. Then the main unit received the signal and gives out chime or alarm sound.

- HOW TO TURN ON OR OFF

Input the secret number followed “#”, the LED will be lighted for 10 seconds that indicate the detecting will be available.

Then if we input again, the LED will flash that indicate the detecting is canceled.

- HOW TO SELECT THE SOUNDS:

  - CHIME--------It gives out “ding dong” sound

  - INSTANT------It give out high decimal alarm sound immediately and last 1

minute.

  - DELAY---------It gives out soft “DI-DI-”sound for 20 seconds then alarm. In

this period you can stop the alarm by input the secret number

followed by “#”.

- HOW TO CHANGE THE SECRET NUMBER

When you put the battery in the main unit, the initial secret number is “0000”.

Then you input the old number “0000﹡”,you will hear a long beep and it tells you that you enter a correct old number. Now you can input a 1-12 digit number followed by “﹡”,then you’ll hear a long beep sound again that indicating you have entered a new number.

- HOW TO MAKE THE ALARM SOUND AT ONCE

When in emergency, we can push the red button “ PANIC”, it will alarm at once for 1 minute.

We can input secret number followed ”#” to stop alarm.