REDCON FASST 8CH Receiver ----FT8RSB

It is REDCON 8CH Receiver with S.BUS port

Specifications:

Model: FT8RSB(8CH FASST receiver with SB Port)

Dimension14.5*47*25mm

Operating Temperature Range: -10℃~60℃

Operating Voltage Range: 3.6 ~9.6V

Operating Current: 70mA max 110mA

Sensitivity:   -96dBm

Weight: 11g (4.5g naked)

Binding
Binding is as easy as holding down the S/F button as you power up the receiver. LED flashes and turns a solid Green when binding completed. Please make sure in binding process the transmitter is on. Another way to Bind is put Binding Plug into Plug channel, then give power to receiver. LED Flashes and turns to solid green, please remove binding plug when binding process completed.

Hint: If disabling failsafe on the transmitter side, FT8RSB will use native failsafe position preset on the transmitter side. After binding, you press the F/S button on Receiver, and LED flash quickly then turn to a solid green when Failsafe setting is completed.

Features:

I. Compatible with FASST 2.4G Air systems both Surface system (C1 Mode) and (7CH/Multi mode)

II. S.Bus Port is compatible with Futaba S.Bus Servo and REDCON S.Bus Servo .

III. Failsafe function is supported, you could set failsafe before fly.