F3_EVO_BRUSH flight controller integrated RC Receiver for QX95 /QX90/QX90C

Receiver configuration:

- Frsky receiver option

Enable Seria_RX for UART2 and Set Receiver mode RX_SERIAL ,Select SBUS in Cleanflight or Betaflight configurator.

Bind procedure:

- Turn on the transmitter , select D8 mode for the Receiver.

- Connect the battery to the board while Jumped the two “BIND” pins on the Board, the green LED will get be solid, this indicates the receiver get into the binding mode.

- Move to the Receiver [Bind] option in the transmitter and ENT to Bind with the receiver, The transmitter beeps.

- The green LED on the board will turning off, this indicates that the bind process was successful. Reconnect the battery for the flight controller, and the green LED on the receiver is solid again. It means connection is established with your transmitter

- Flysky Receiver Option

Just Set Receiver mode to be RX_PPM

Bind procedure:

- Connect the battery to the board while Jumped the two “BIND” pins on the board, the green LED will flash fast, this indicates the receiver get into the binding mode.

- Set receiver mode to AFHDS for your radio, then get your radio to binding mode.

- The green led on the board will getting to be solid ,this indicates binding successful.

- Reconnect the flight controller and the battery ,the green LED on the board flash fast again, this indicates connection is established with your transmitter.

- DSM2 Receiver Option

Just Set Receiver mode to be RX_PPM and select SPEKTRUM1024

Bind procedure:

This DSM2 version has an "auto-bind" procedure just like with small toy Quadcopter . First Connect the battery to the flight controller, waiting board to get into binding mode . The blued LED will blinking slowly ,and it will blinking fast soon , this indicate the board is in Binding mode , turn on the transmitter and Enter into Binding mode, the Blue LED on the receiver will turn off and then get be solid ,this indicate binding successfully .

If you flashed the firmware or erase chip, please first do the bellowing procedure , don’t connect the battery otherwise the motor will auto-spin

- Cleanflight: Go to the CLI tab, type “Set motor_pwm_rate=1000” ,then enter save

Betaflight: Go to Configure Tab and set ESC/Motor protocol to BRUSHED

*This step is in order to avoid motor auto-spinning when connect the battery