F3_EVO_BRUSH flight controller integrated RC Receiver for QX90/QX90C/QX95

Dimension: 22mm*32.5mm
Thickness: 1.2mm

Weight: 3g

Integrated receiver option:

Flysky 6CH PPM Receiver(AFHDS 2A)

Coreless motor plug: SH1.0

Firmware: SP RACING F3 EVO 1.13.0

Support work voltage: 7.0~8.4v(2S Lipo battery)

Features:

- F3_EVO_Brush revision is out of the F3 EVO SP RACING is based on a SP RACING F3 EVO firmware 32 brush flight control.ler

- Independent design of the circuit structure

- Using STM32F303CCT6 + MPU6500, advanced hardware platform F3 guarantee more stable flight.

- With a large and high quality current NMOS transistors, operating current of up to 10A or more. Each Brushed motor is equipped with freewheeling diodes.

- Integrated 2.4G receiver, there are 3 types receiver option to choose.

- With battery voltage detection and buzzer interface(solder pad)

- LED_STRIP Function(solder pad)

Connection diagram:

Notice:  New release AFHDS 2A Controller remove bind pins and Add a binding button

Receiver configuration:

- Flysky Receiver Option

Just Set Receiver mode to be RX_PPM

Bind procedure:

- Connect the battery to the flight controller while holding the binding button on the board ,the Blue LED will blinking fast, this indicates the Receiver is in binding mode. Then release the binding button.

- Turn on your radio and Set receiver mode to AFHDS 2A, then get your radio into binding mode. The blue LED on the flight controller will turning off for a second and the starting to blinking slowly, this indicates binding successfully.

- Turn on your radio ,then Reconnect the flight controller and the battery ,the Blue LED on the flight controller board will getting to be solid ,this indicates connection is established with your transmitter.

If you flashed the firmware or erase chip, please first do the bellowing procedure , don’t connect the battery otherwise the motor will auto-spin

- Cleanflight: Go to the CLI tab, type “Set motor_pwm_rate=1000” ,then enter save

Betaflight: Go to Configure Tab and set ESC/Motor protocol to BRUSHED

*This step is in order to avoid motor auto-spinning when connect the battery