Specification:

-Brand name: Eachine

-Item Name: Teenycube DSM2/X satellite Receiver

-Frequency range: 2.403-2.479Ghz

-Input power: 5V

-Response time: 22ms / 11ms

-Resolution: 1024/2048

-Display method: LED

-Operating voltage: 3.3V

-Working current: 60MA

-Size: 20mm*20mm*5mm

-Weight: 1.1 g

-Antenna length: 50mm

-Data format: Serial port

-Protocol: DSM2/DSMX

-Distance: no ground interference (1 m from the ground ) > 200m

-Uses: indoor small aircraft.

-Compatible Transmitters: DSM2 / DSMX series of remote control

Pin-out diagram:

Bind procedure With Teenycube F3 flight controller:

-Connect Flight controller to computer and open Betaflight or Cleanflight configurator From CLI tab type: "set spektrum_sat_bind = 9" for DSMX or "set spektrum_sat_bind = 5" for DSM2

-Type "save" and after Flight controller reboot remove USB cable (=Power off the board)

-Wait a second and reconnect the USB cable. After cold start satellite led(Orange color LED) should start blinking and transmitter should be turned on while pressing the bind button

-After binding satellite led should be solid. Connect Betaflight and use receiver tab to test that satellite is working correctly.

-Final step is to go to CLI tab and type "set spektrum_sat_bind = 0" and then type "save". This must be done so that satellite doesn't go back to binding mode when the Flight controller is repowered again.