Specification:

-Brand Name: Eachine
-Item Name: Teenycube Frsky receiver

-Frequency range: 2.403-2.479Ghz

-Channels:8CH

-Work mode :D8 Mode
-Output: SBUS/PPM Switchable

-Antenna length: 50mm
-No ground interference ( Transmitting and receiving 1 m from the ground): >200m

-Working current: 80mA
-Dimensions: 20*20*5mm

-Weight: 1.2g
-Compatible with FRSKY ACCST 
-Compatible with X9D(Plus)DJT/DFT/DHT

Pin-out diagram:

Binding procedure:

-Power for the Receiver while holding the Bind button, the blue LED on the receiver will getting to be solid, this means the receiver is in binding mode, then release the Bind button.

-Turn on your Radio and select D8 mode for the Receiver. Then Go to the Receiver [Bind] option, and ENT to Binding with the Receiver. The Blue LED on the receiver will turning off, this indicates binding successfully.