M1 no hole HD 1080P charging head camera manual

Thank you for using the company's products! Please read the instruction before using this product. For better services, the contents of this user manual may be changed. Because of the product's performance and function, the change will not be notified.

This product is the first fool type no hole charger camera. Products without any key, connect power supply, automatic camera, pull point power, automatically stop saving video files. Products HD digital camera, 1920*1080P imaging, built-in storage card 4G to 32G can be matched, the charger can be shot while the video side to the phone and other electronic products. Automatic cycle camera (when the memory is full, delete the earliest video files, keep the latest video files). Video synchronization (video and audio synchronization). This product is simple and elegant, beautiful and practical, easy to carry, is the home security, education, life and other areas of the necessary practical tools, by the user's favor.

Product structure sketch map:

1: Camera: machine connection socket, red and blue light blue lights flashing lights at the same time, after three time put out, representative to enter the camera state, the machine from the socket pulled out, the lights flashing three out, stop and save the camera on behalf of.

2: Electronic equipment charge: the product can be in the camera during the same time data cable connection USB interface, can give electronic products.

3: Video Sync: video and audio synchronization.

4: Automatic cycle camera: when the memory is full, the machine will delete the earliest video files, will retain the latest video files.

5: Reset: when the machine appears dead, the indicator lights, the machine from the socket, about a minute later, the lights out, the machine will automatically reset.

6: Time change: camera provides the video file to display the time of the function, you can set the time according to the actual needs of the time format for the year. Set the following method: connect the computer, find the mobile disk, click the right button on the disk space to move the mouse to the pop-up menu on the new ". You can also create a copy of this folder on your computer desktop as described above and then copy it to the disk folder. Open the time folder, set the time format, such as: 00:00:00 2000.01.01, year, month, day and hour, minute, second, separated by space. Then save. Save the file after the security exit hardware, boot, time settings to complete. Time set up, the time of the video file with you set the time to. Note: the time is set up after a certain time to start to take effect.

Related parameters:

Video format         AVI

video coding         M-JPEG

Video resolution      1920*1080

Playing software      Operating system comes with or mainstream video player software

Image proportion     4:3

Storage support       1G 2G 4G 8G 16G 32G TF Card