# YTech 2.4G CC2500 NRF24L01 A7105 CTRF6936 4-IN-1 Multi-protocol STM32 TX Module With Antenna

Overview:

This 2.4G Multi-protocol TX Module is STM32 ARM microcontroller based module. All available protocols are included in serial mode. It is suitable for many brand of quadcopters, helicopters and airplanes.

There are two modes to use the Module: PPM mode and serial mode.

Parameters：

Operating voltage:5-14V                              Operating current: <=100mA

Operating frequency: 2.4G ISM band                    RF power: +22dBm

MCU: STM32F103CBT6 (128K ROM, 20K RAM)        Case: not include, be on sell later

Size: 55x41x7mm, button not include                    Weight: 23g

Normal use operation in PPM mode:

- Install RF Module in position, Set PPM signal output on you transmitter.

- According to the default protocols table, turn protocol switch of RF module to choose the protocol.

- After finish binding operation, Power on your transmitter, the red light of RF module will be on, then RF module is ready to work , after that power on your receiver (or craft).

Binding operation in PPM mode:

- Power on your receiver, and set it to binding mode.

- Hold and press the bind button of RF module, and then turn on your transmitter, after 2 seconds, release the button, you will see the red light flashing rapidly, then RF module is in binding mode, and the red light will go solid after binding.

- Some protocols (eg: S-FHSS) don’t have binding procedure on RF module, and some protocols (eg: hubsan, e010)will auto bind when power up.

Operation in Serial mode:

Turn the protocol switch to“0“ to access serial mode, in serial mode all available protocols are included. Transmitter that supports the er9X/erSky9X or OpenTX firmwares can work in this mode, for more information, Please refer to the Link below.

https://github.com/pascallanger/DIY-Multiprotocol-TX-Module

About protocols:

When in PPM mode, there are 15 different protocols mapping To the 16-position protocol selection switch on the module. They are listed in the default protocols table on the last page, and You can customize these when you compile you own firmware.

For more information, You can visit :

https://github.com/pascallanger/DIY-Multiprotocol-TX-Module/blob/master/Protocols_Details.md

Introduction:

This module integrate four RF chips (CC2500,NRF24L01,A7105,CYRF6936) into one single circuit board, it .supports a variety of remote control protocols ,such as Futaba S-FHSS, Walkera DEVO, Spektrum DSM2, DSMX, Flysky, Frsky, WLToys, Hubsan, Hisky, Esky , Assan etc. You can control your craft flexibility with it , and You will get much excellent experience with you favorite transmitter.

Thanks to all the developers for their great job on protocols. The following is an excerpt from Pascal langer’s readme file of Multi- module project:.

The MULTI-Module supports industry standard PPM interface that works with all transmitters with either

a module bay or a trainer port or any PPM signal that can be accessed inside the Tx.

Most of the older FM radios support the PPM interface.

If you are the owner of a transmitter that supports the er9X/erSky9X or OpenTX firmwares (Frsky Taranis, Horus or the FlySky TH9X or the Turnigy 9X family) you have the additional option to use a serial protocol to communicate between your Tx and the MULTI-Module. (Owners of Walkera Devo transmitters should look at the Deviation Tx project for how to achieve the same end goal). This serial protocol does not require any hardware modifications, but will likely require updating the firmware on your radio. For those willing to do this, there are some nice advantages:

  The model protocol selection and binding is done from the Model Settings menu on the Tx

  For telemetry capable transmitters, the telemetry integration is done seamlessly with the Tx firmware.

Notice:

- The green light on the module is reserved for future use

- You can update the firmware of module by yourself, if you want to do that, you should set the jumpers properly, like these patterns below:

Default protocols table for PPM mode:

| Dial 开关档位 | Protocol 协议 | Sub_protocol 子协议 | Auto Bind 自动对频 | Option 选项 | RF Chip 射频芯片 |
| --- | --- | --- | --- | --- | --- |
| 0 | Reserved | - |  |  |  |
| 1 | FLYSKY | FLYSKY | No/否 | 0 | A7105 |
| 2 | HUBSAN | - | Yes/是 | 0 | A7105 |
| 3 | AFHDS2A | PPM_SBUS | No/否 | -10 | A7105 |
| 4 | FRSKYD | - | No/否 | 0 | CC2500 |
| 5 | FRSKYX | CH_8 | No/否 | 0 | CC2500 |
| 6 | S-FHSS | - | No/否 | 10 | CC2500 |
| 7 | DSM2 | DSM2_22 | No/否 | 6 | CYRF6936 |
| 8 | DEVO | - | No/否 | 0 | CYRF6936 |
| 9 | J6PRO |  | No/否 | 0 | CYRF6936 |
| A | ESKY |  | No/否 | 0 | NRF24L01+ |
| B | HISKY | Hisky | No/否 | 0 | NRF24L01+ |
| C | KN | WLTOYS | No/否 | 0 | NRF24L01+ |
| D | V2X2 | V2X2 | Yes/是 | 0 | NRF24L01+ |
| E | MJXQ | E010 | No/否 | 0 | NRF24L01+ |
| F | ASSAN | - | No/否 | 0 | NRF24L01+ |

All available protocols for serial mode:

| protocol 协议 | sub_protocol 子协议 | Auto Bind 自动对频 | Option 选项 | RF Chip 射频芯片 | Reference 说明 |
| --- | --- | --- | --- | --- | --- |
| FLYSKY |  | NO/否 | 0 | A7105 | FLYSKY/富斯一代 |
| HUBSAN |  | YES/是 | 0 | A7105 | HUBSAN/哈博森 |
| AFHDS2A | PWM_IBUS | NO/否 | 0 | A7105 | FLYSKY AFHDS2A/富斯二代 |
|  | PPM_IBUS | NO/否 | 0 | A7105 |  |
|  | PWM_SBUS | NO/否 | 0 | A7105 |  |
|  | PPM_SBUS | NO/否 | 0 | A7105 |  |
| FRSKYD |  | NO/否 | -10 | CC2500 | FRSKY D8 |
| FRSKYX | CH_16 | NO/否 | -10 | CC2500 | FRSKY D16 |
|  | CH_8 | NO/否 | -10 | CC2500 |  |
| FRSKYV |  | NO/否 | -10 | CC2500 |  |
| S-FHSS |  | NO/否 | 10 | CC2500 | Futaba |
| DSM | DSM2_22 | NO/否 | 6 | CYRF6936 | DSM2,22mS |
|  | DSM2_11 | NO/否 | 6 | CYRF6936 | DSM2,11mS |
|  | DSMX_22 | NO/否 | 6 | CYRF6936 | DSMX,22mS |
|  | DSMX_11 | NO/否 | 6 | CYRF6936 | DSMX,11mS |
| DEVO |  | NO/否 | 0 | CYRF6936 | walkera/华科尔 |
| J6PRO |  | NO/否 | 0 | CYRF6936 | Nine eagles/九鹰 |
| HISKY | Hisky | NO/否 | 0 | NRF24L01+ | Hisky/驰远 |
|  | HK310 | NO/否 | 0 | NRF24L01+ |  |
| V2X2 | 无 | NO/否 | 0 | NRF24L01+ |  |
| YD717 | YD717 | NO/否 | 0 | NRF24L01+ |  |
|  | SKYWLKR | NO/否 | 0 | NRF24L01+ |  |
|  | SYMAX4 | NO/否 | 0 | NRF24L01+ | SYMA/司马 |
|  | XINXUN | NO/否 | 0 | NRF24L01+ | XINXUN/鑫讯 |
|  | NIHUI | NO/否 | 0 | NRF24L01+ | NIHUI/霓辉 |
| KN | WLTOYS | NO/否 | 0 | NRF24L01+ | WLTOYS/伟力 |
|  | FEILUN | NO/否 | 0 | NRF24L01+ | FEILUN/飞轮 |
| SYMAX | SYMAX | NO/否 | 0 | NRF24L01+ | SYMA/司马 |
|  | SYMAX5C | NO/否 | 0 | NRF24L01+ |  |
| SLT |  | NO/否 | 0 | NRF24L01+ |  |
| CX10 | CX10_GREEN | NO/否 | 0 | NRF24L01+ | CX/澄星 |
|  | CX10_BLUE | NO/否 | 0 | NRF24L01+ |  |
|  | DM007 | NO/否 | 0 | NRF24L01+ |  |
|  | Q282 | NO/否 | 0 | NRF24L01+ |  |
|  | JC3015_1 | NO/否 | 0 | NRF24L01+ |  |
|  | JC3015_2 | NO/否 | 0 | NRF24L01+ |  |
|  | MK33041 | NO/否 | 0 | NRF24L01+ |  |
|  | Q242 | NO/否 | 0 | NRF24L01+ |  |
| CG023 | CG023 | NO/否 | 0 | NRF24L01+ |  |
|  | YD829 | NO/否 | 0 | NRF24L01+ |  |
|  | H8_3D | NO/否 | 0 | NRF24L01+ |  |
| BAYANG |  | NO/否 | 0 | NRF24L01+ |  |
| ESKY |  | NO/否 | 0 | NRF24L01+ | ESKY/易思凯 |
| MT99XX | MT99 | NO/否 | 0 | NRF24L01+ |  |
|  | H7 | NO/否 | 0 | NRF24L01+ |  |
|  | YZ | NO/否 | 0 | NRF24L01+ |  |
|  | LS | NO/否 | 0 | NRF24L01+ |  |
| MJXQ | WLH08 | NO/否 | 0 | NRF24L01+ | MJX/美嘉欣 |
|  | X600 | NO/否 | 0 | NRF24L01+ |  |
|  | X800 | NO/否 | 0 | NRF24L01+ |  |
|  | H26D | NO/否 | 0 | NRF24L01+ |  |
|  | E010 | YES/是 | 0 | NRF24L01+ | E010/JJRC H36 |
| SHENQI |  | NO/否 | 0 | NRF24L01+ |  |
| FY326 |  | NO/否 | 0 | NRF24L01+ |  |
| FQ777 |  | NO/否 | 0 | NRF24L01+ |  |
| ASSAN |  | NO/否 | 0 | NRF24L01+ |  |
| HONTAI | FORMAT_HONTAI | NO/否 | 0 | NRF24L01+ |  |
|  | FORMAT_JJRCX1 | NO/否 | 0 | NRF24L01+ |  |
|  | FORMAT_X5C1 | NO/否 | 0 | NRF24L01+ |  |
|  | FORMAT_FQ777_951 | NO/否 | 0 | NRF24L01+ |  |