Teenycube F3T 6DOF integrated PDB 20x20mm flight controller

Feature:

STM32 F303 MCU

Firmware version: Betaflight 3.1

Firmware target: Omnibus

ESC Dshot protocol compatible(Need not modify)

SBUS/PPM/DSM2/DSMX input (Pin headers)

4PWM output (Pin headers)

Super Tiny Only 20x20mm, mount holes 15x15mm M2 screw

SPI Sensor MPU6000

2-4S Lipo Direct power

5V@1A BEC

3.3V output for spectrum Satellite Receiver

Built-in PDB

LED Strip solder pad ready

Buzzer solder pad ready

Weight: only 1.6g

Best for 60mm-80mm brushless frame

Pins connection diagram:

Top view                             Bottom view

Getting start:

1. Install latest STM32 Virtual COM Port Driver

http://www.st.com/web/en/catalog/tools/PF257938

2. Install and launch the Cleanflight Configurator tool

https://chrome.google.com/webstore/detail/betaflight-configurator/kdaghagfopacdngbohiknlhcocjccjao?utm_source=chrome-ntp-icon	(you need to open this link in Google Chrome. If you don’t have Google Chrome, download and install this first)

3. Connect the flight controller to the computer via USB cable.

4. Select the correct COM port if it is not automatically detected.

5. Click connect, verify that communication is established

Software:

The Teeny F3T flight controller runs the Open-source Betaflight flight control (FC) software . The newest version is Betaflight 3.1 which supports DSHOT very well .

HEX Firmware target:

https://github.com/betaflight/betaflight/releases/download/v3.1.6/betaflight_3.1.6_OMNIBUS.hex

DFUSE tools:

http://www.st.com/zh/development-tools/stsw-stm32080.html

DFUMODE to flash firmware should first Connect the boot pad and install the STM32 Bootloader driver.

Receiver Configurations

- SBUS Receiver:

Connect your SBUS receiver to [RCIN +5V GND] port; Enable Serial_RX for UART3 from the Port tab in Betaflight configurator, then select RX_SERIAL from the RECEIVER Mode and set the Serial Receiver Provider to be SBUS in Betaflight Configurator.

- PPM Receiver:

Connect your PPM receiver to [RCIN +5V GND] port and then set the Receiver Mode to RX_PPM from the configuration in Betaflight configurator.

- Spektrum Satellite DSM2/DSMX or Receiver

Connect your DSM2/DSMX receiver to [RCIN +3.3V GND] port; Solder the power switchable pins(pin1+pin2) from the bottom side of the flight controller to get 3.3v output for the receiver; Enable Serial_RX for UART3 from the Port tab in Betaflight configurator, then select RX_SERIAL from the RECEIVER Mode and Select SPEKTRUM1024 for DSM2 Radio; Select SPEKTRUM2048 for DSMX Radio in Betaflight Configurator.

Spektrum satellite DSM2/DSMX Receiver binding procedure :

(1)	Connect your receiver to the Teeny flight controller then Connect Teeny F3T to computer and open Betaflight configurator, From CLI tab type: "set spektrum_sat_bind = 9" for DSMX radio or "set spektrum_sat_bind = 5" for DSM2 radio

(2)	Type "save" and after Flight controller reboot remove USB cable (=Power off the board)

(3)	Wait a second and reconnect the USB cable. After cold start satellite led(Orange color LED) should start blinking and transmitter should be turned on while pressing the bind button

(4)	After binding satellite led should be solid. Connect Betaflight and use receiver tab to test that satellite is working correctly.

(5)	Final step is to go to CLI tab and type "set spektrum_sat_bind = 0" and then type "save". This must be done so that satellite doesn't go back to binding mode when the Teeny F3T is repowered again.

Useful Links:

https://github.com/betaflight/betaflight/wiki