Technical data:

( Manual time setting.

( Temperature alternatively in ℃ or ℉.

( 12/24 hour time display.

( Thermometer: Indoor measurement ranges: 0°C (32°F) ~ 50°C (122°F)

outdoor measurement ranges: -39.9°C (-39.8°F) ~ 59.9°C (139.8°F)

( Display MIN/MAX In/Outdoor Temperature

( Battery: 2 x AAA /LR03 (not Included).

LCD SCREEN AND SETTINGS:

Wireless remote sensor (transmitter)

( Transmitter frequency: 433.92 MHz.

( Range of transmission is up to 60m (200feet).

( Iinsert the 2 batteries in to the transmitter, Pay attention to observe the correct polarity.

Initial operation:

( Open the battery compartment on the rear side of the outdoor remote sensor and insert the batteries. Pay attention to observe the correct polarity. Select the °C/°F display by pushing the button inside the compartment. Close in the battery compartment

( Open the battery compartment on the rear side of the receiver and insert the batteries. Pay attention to observe the correct polarity. Close the battery compartment.

( When you insert the batteries, all the icon on the LCD display will briefly light up for 3 seconds.

( The receiver will now start to make a connection to the outdoor remote sensor. This operation takes about 3 minutes and is displayed by a flashing reception RF antenna symbol in the “OUTDOOR” display area on the receiver.

FUNCTION KEYS:

Manual time setting:

( Press “SET ” for about 3 seconds to confirm your setting, the 12/24 hour mode display starts to flash. Now use “+” buttons to set the correct 12/24 hour mode.

( Press “SET” again to confirm your setting, the Hour display starts to flash. Now use “+” buttons to set the correct hour.

( Press “SET ” again to confirm your setting, the Minute displays starts to flash. Now use “+” buttons to set the correct minute.

( Press “SET” again to confirm your setting and to end the setting procedures, enter the clock mode.

F.Y.I.:

( After 30 seconds without pressing any button, the clock switches automatically from Set Mode to Normal Time Mode.

°C/°F temperature display:

( The temperature is displayed either in °C or °F. Briefly pressing the “°C/°F “button allows you to switch between the individual models.

Maximum/Minimum Temperature display:

( To toggle indoor/outdoor maximum, press the “MEM” button.

( Once to show the maximum indoor/outdoor temperature values.

Twice to sow the minimum indoor/outdoor temperature values

Three times to return to the current temperature levels

( To reset the maximum and minimum temperature, press and hold down the “MEM” button about 3 seconds. This will reset all minimum and maximum data recorded to the current displayed values.

IN/OUT temperature display:

( The in door temperature or out door temperature is displayed of the LCD . Briefly pressing the “IN/OUT “key allows you to switch between the individual models.