Available protocols (incomplete and expanding)

| NO. 编号 | Protocol 协议 | Sub_protocol 子协议 | RF Chip 射频芯片 |
| --- | --- | --- | --- |
| 1 | FLYSKY | FLYSKY V9X9 V6X6 V912 CX20 | A7105 |
| 2 | AFHDS2A | PWM PPM IBUS SBUS | A7105 |
| 3 | HUBSAN | NONE | A7105 |
| 4 | FRSKYV | NONE | CC2500 |
| 5 | FRSKYD | NONE | CC2500 |
| 6 | FRSKYX | CH_8 CH_16 EU_8 EU_16 | CC2500 |
| 7 | S-FHSS | NONE | CC2500 |
| 8 | DSM | DSM2_11 DSM2_22 DSMX_11 DSMX_22 | CYRF6936 |
| 9 | DEVO | NONE | CYRF6936 |
| 10 | WK2X01 | WK2801 WK2401 | CYRF6936 |
| 11 | J6PRO | NONE | CYRF6936 |
| 12 | ESKY | NONE | NRF24L01+ |
| 13 | HISKY | HISKY HK310 | NRF24L01+ |
| 14 | KN | WLTOYS FEILUN | NRF24L01+ |
| 15 | V2X2 | V2X2 JXD506 | NRF24L01+ |
| 16 | ASSAN | NONE | NRF24L01+ |
| 17 | MJXQ | WLH08 X600 X800 H26D E010 H26WH | NRF24L01+ |
| 18 | YD717 | YD717 SKYWLKR SYMAX4 XINXUN NIHUI | NRF24L01+ |
| 19 | SYMAX | SYMAX SYMAX5C | NRF24L01+ |
| 20 | SLT | SLT VISTA | NRF24L01+ |
| 21 | CX10 | GREEN _BLUE DM007 JC3015 MK33041 | NRF24L01+ |
| 22 | CG023 | CG023 YD829 H8_3D | NRF24L01+ |
| 23 | BAYANG | BAYANG H8S3D | NRF24L01+ |
| 24 | MT99XX | MT99 H7 YZ LS FY805 | NRF24L01+ |
| 25 | SHENQI | NONE | NRF24L01+ |
| 26 | FY326 | FY326 FY319 | NRF24L01+ |
| 27 | FQ777 | NONE | NRF24L01+ |
| 28 | HONTAI | HONTAI JJRCX1 X5C1 FQ777_951 | NRF24L01+ |
| 29 | Q2X2 | Q222 Q242 Q282 | NRF24L01+ |
| 30 | Q303 | Q303 CX35 CX10D CX10WD | NRF24L01+ |
| 31 | GW008 | NONE | NRF24L01+ |
| 32 | DM002 | NONE | NRF24L01+ |
| 33 | ESKY150 | NONE | NRF24L01+ |
| 34 | CORONA | COR_V1 COR_V2 FD_V3 | CC2500 |

Parameters：

Operating voltage:5-9V                          Operating current: <=180mA

Operating frequency: 2.4G ISM band               RF power: +22dBm

MCU: STM32F103CBT6(128K ROM, 20K RAM)    Weight: 32g

Introduction:

This 4-in-1 TX  module is suitable for FRSKY X-Lite. It integrates four RF chips (CC2500,NRF24L01+,A7105,CYRF6936) into one single circuit board, it supports a variety of remote control protocols, such as Futaba S-FHSS, Walkera DEVO, Spektrum DSM2, DSMX, Flysky, Frsky, WLToys, Hubsan, Hisky, Esky , Assan etc. You can control your model flexibility with it, and you will get much excellent experience with you favorite transmitter.

This module is compatible with the Multi-module project on github. It’s based on STM32 microcontroller. All available protocols are included in serial mode. In this mode, it uses a serial protocol to communicate with your transmitter. The serial protocol does not require any hardware modifications, but you should update the firmware on your transmitter to the latest. Then the model protocol selection and binding is done from the Model Settings menu on your transmitter. For telemetry capable transmitters, the telemetry integration is done seamlessly with the transmitter firmware.

For more information, please scan the QR code to access :

How to use:

- Refer to the website above, update your transmitter with proper firmware.

- Screw down the antenna of module tightly, and then install TX Module to the module bay of your transmitter.

- Power on your transmitter, enter Model Settings menu, turn on External RF , and select ‘MULT’ mode, then you will see the bind and protocol button in the menu, and then you can choose a proper protocol for you model and bind with it now.

LED State:

| Green Led | Red Led | Status |
| --- | --- | --- |
| OFF | Flashing raipidly | Bootloader is running, please wait |
| ON | ON | Normal or Range Check |
| ON | Flashing slowly | No serial input |
| ON | Flashing raipidly | Binding |

Notice:

- Make sure to check the ‘multimodule’ option, when you update OpenTX firmware through Companion software.

- In serial mode, for FRSKY and S-FHSS protocol, you may need set the value of Fine or Option (in Model Settings menu on your TX) properly to bind with your model. The value can be varied, since it’s partly depended on your model.