Voltage: DC+12V

Coin Diameter: 18mm~31mm

Coin Thickness: 1.2mm~3.1mm

1.     Put on sample coin.

2.     Adjust entry slot opening to your coin size by loosening screw on the back of 
      metal panel for blocking bigger invalid coin from inserting.

3.     Turn the screw on front lid in clockwise direction for ditching “thinner coin” 
      through the slot of lid if necessary.

4.     switch to Normal Open (N.O.) or Normal close (N.C) for signal output of 
coin validation upon Host requested .

5.     3 triggering TIMER SWITCH of Pulse Duration ,

Long duration of Pulse   :. 100ms

Common duration of Pulse : 50ms

Short duration of Pulse    :30ms

6.     VR tuning for tolerance of coin acceptance , turn clockwise for slack and anti-
       clockwise for precise acceptance.

7.     Shift sensitivity switch of coin acceptance downward to “special” to extend 
      the range of discriminated ratio for twin metal coins or the coins in big    
      tolerance.