Bluetooth Watch Instructions

Thank you for choosing our U8 devices. You can read the manual, a comprehensive understanding of the use of equipment, in fact, with a taste of the function and simple method of operation.

This device is used as long as the brand of intelligent machines are adapted to use intelligent machines can synchronize phonebook and provides a variety of useful features and services to facilitate your work and leisure activities in the smart machine operation.

The Company reserves the right to make any prior notice in the case of the contents of this manual for the right to amend, without notice.

When you get a U8 , and install “ Smartwatch.apk” program on the smart phone, realize SMS, LINE, Facebook, Instugrate,Facebook Message, QQ, weather forecasts and other instant messaging reminders.

APK Access mode 1：Download by using Smart phone to scan the two-dimensional code below

APK Access mode 2：Download from Web address

IP Address: www.myuwatch.com/Smart_Watch.apk

After installing “Smartwatch.apk”, and smart phone connect to watch ,First open Bluetooth function of your smart phone and watch  , phone will search watch Equipment name and initiate a connection，next smart phone will send "Bluetooth pairing request" and then you press  "confirm" for pairing ,After pairing watch will prompt "**（Connected）" ，About 5 seconds later the watch will prompt "sync date&time with remote" (functions of synchronousing date and time required to install " Smartwatch.apk" in the smart phone )，while there is a  " " icon in the standby interface ,which indicates a successful connection between your smartphone and watch, After a successful connection you can operate watch according to the following steps

※ The whole machine institutions to introduce

Power on or off key/HOME key ~ Long press this button to start power on/off,  Short Press to return to the standby interface.

Back key/Hang up key ~ click to back to previous menu or hang up when calling

Volume key ~ click to pop-up volune adjustment interface

Confirm/answer key ~ Standby interface click to enter the main menu, confirm key in the main menu,answer key when calling.

Microphone ~ Don't keep out the hole while calling.

USB port ~  battery charging.

Speaker ~ Don't keep out the hole while calling.

RESET hole ~ click on this key to achieve the system reset when the watch is abnormal.

※ Introduce the main menu：According to watch the main function is divided into 4 page

First page:Bluetooth, Phonebook, Dialer, Messaging;

Second page:Call log, Notification, Music, Remote capture;

Third page:Settings,Anti lost,Power saving,Ringtone;

Fourth page:Barometer, Altimeter, Pedometer,Stopwatch.

Function information:

● Bluetooth:Open this function will see the following menu

- Bluetooth dialer ~ search and a matching connection with bluetooth devices

- Bluetooth settings ~ Bluetooth can be turned on and off set and the machine equipment name display

●Phonebook:The watch is connected with the mobile phone will display mobile phone contacts in the machine(can display 1000)

●dialer: Watch is connected to the phone can dial

●Messaging:Open this function will see the following menu,This function needs to install the " Smartwatch.apk " application for use in mobile phone terminal.

- Inbox: Show a mobile phone short message

- Sent messages: Show a mobile phone sent message

●Call log: Open this function will see the following menu

1）Missed calls ~ Display the missed call ,At the same time can call the corresponding contact

2）Dialed calls ~ Display the dialed call,At the same time can call the corresponding contact

3）Received calls ~ Display the received call,At the same time can call the corresponding contact

4）All calls ~ Display mobile phone calls all phone records

●Notifier:Can query the QQ/ Wechat and other timely news,This function needs to install the " Smartwatch.apk" application for use in mobile phone terminal.

●Music:Can control the music playing in the mobile phone

●Camera:Remote on/off mobile phone camera press confirm to complete pictures

●Settings:Open this function will see the following menu

- Clock type ~ For analog and digital clock selection.

- Set Time ~ Can set up time.

- Set Date ~ Can set up date.

- About watch ~ Display mobile phone software version information.

●Anti lost:Watch wil shake alarm after keep away from the mobile phone for a certain distance,Open this function will see the following menu.

- Enable

●Power save:Open this function the use of the time of the watch will be more durable

●Ringtone:For different state set ringtones,Open this function will see the following menu.

- Mute

- Vibration

- Ring1

- Ring2

- Ring3

●Barometer:Open this function to display the current atmospheric pressure altitude and the current temperature.

●Altimeter:Calculation of vertical to watch moving downward relative height after a certain distance,Open this function will see the following menu

- Cur_Alitmeter(m)~

- Set start altitude~ Click the menu setting initial height,Then the vertical upwards or downwards Watch

- Relative Alitmeter(m) ~ Display watch the relative height after vertical upward or downward

●Pedometer:Calculation of the walking distance of time (time, minutes, seconds) and the number of kilometers (km),Open this function will see the following menu.

- Pedometer ~ After entering the menu then press the mechanical keys trigger timing starts

- Last Record ~ Record the minutes of the last walking time and mileage

- Step Setting(CM) ~ According to height ratio setting step distance

●Stopwatch:Open this function can be timing.

●Menu Style: Can change the Menu Style pisplay of the watch

●ClockStyle: Can change the clock pisplay of the watch

●Find phone: The phone will ring as soon as open this function(iphone disable)

●TimeDate: Can set the time and the date of the watch.

Tip:This product's battery is non-removable.And maybe the product cann't power on when it is idle for more than a month on account of  the wastage of itself.Please charge your device.