Enter the corresponding          Press the SET key to choose the

Programmable item, the          programmable value, the RED LED

RED LED flashes for several      flashes for several times, the times

Times, the times presents the      presents the serial number o the value

Current value of this time         you are choosing.

Release                       Press

SET key                      SET Key

Hold SET key for 3 seconds

Release 	       Press

SET Key              S    Set key                             Set key

Hold SET key for 3 seconds

Release 	Press

SET Key   	Setkey

Hold SET key for 3 seconds

Release                         Press

SET Key                        SET key

If the N1 is bigger than number 5, we use a long time flash

so it is easy to identify the items of the big number.

For example, if the LED flashes as the following:

A long time flash + a short time flash = the No.6 item

A long time flash + 2 short time flash = the No.7 item

A long time flash + 3 short time flash = the No.8 item

And so on.

# Text boxes

Turn off the ESC

Turn on the transmitter

Hold the SET key,

Switch on the ESC

Red LED flashes

Green LED flashes

For 1 time

Enter the 1st item

“Motor Timing”

Red LED flashes for 1 time to choose “Very Low”

Red LED flashes for 2 times to choose “Low”

Red LED flashes for 3 times to choose “Normal”

Red LED flashes for 4 times to choose “High”

Red LED flashes for 5 times to choose “Very High”

Finish programming, switch off the ESC, and then switch it on

Green LED flashes

For 2 times

Enter the 2nd item

“Initial Acceleration”

Red LED flashes for 1 time to choose “Low”

Red LED flashes for 2 times to choose “Medium”

Red LED flashes for 3 times to choose “High”

Red LED flashes for 4 times to choose “Very High”

Green LED flashes

For 3 times

Enter the 3rd time

“Runing Mode”

Red LED flashes for 1 time to choose “Forward with brake”

Red LED flashes 2 times to choose “Fwd/Rev with brake”

Red LED flashes for 3 times to choose “Forward/revese”

……The following steps are just live the above steps…….

Green LED flashes

for N times

Enter the Nth item

Press SET key to choose the value, the flash time of RED LED means the serial number of value (1 time means the 1st value, 2 times means 2nd value….)