Overview

●Refined exterior design

Unique design fits for hand.

●Multi file format support!

This player recognize MP1, MP2, MP3, WMA and video in WMV, ASF, WAV and AMV formats.

●Firmware upgrade available

You can download and upgrade software from website enhancing player’s function.

●FM stereo radio

Powerful automatic or manual tuning capability, save up to 40 channels (20 channels in each system).

●e-Documents

You can download text files into the player

●Driver free USB memory

Manage your files in USB memory without specified software, no need drivers in WIN2000 or furthers.

●’Secret Space’

You can separate part of the memory encrypting and hiding in using programs provided, where data

cannot be seen or written by others.

●Recorder / Repeat

Voice can be recorded and saved in WAV or ACT format. Snippet/Contrast repeat available.

●Equalizer

Normal, Rock, Pop, Classic, Soft, Jazz, Bass

●Backlight colors

This player provides 7 backlight colors.

● Play modes

Normal, Single Repeat, Play Catalog, Repeat Catalog, Repeat All, Shuffle, Lyric.

●Timing turning off

The player provides Sleep and battery saving mode, more convenience for you!

●Complete dynamical menu

Visualized dynamical menus with text instructions make you easy control.

# Declarations

Please read this manual carefully.

Functions and performance may change without prior notice.

Know your player

## Exterior and Key

1. SPEAKER

2. EARPHONE

3. USB

4. MENU/MODE

5. NEXT/VOL+

6. POWER ON/OFF

7. PLAY/PAUSE/STOP

8. VOL

9. LAST/VOL-

## Displayer

## Battery Level

The player shows capacity in 9 levels

Battery is full on 3.8V. As time goes on, capacity indication will monish.

Indicator shows blank when battery almost ran out. You should charge your battery at that time.

Please switch on the player before charge. This player cannot be charged in case of power off/

Please switch off power when not using the player.

Basic Functions

- Access to Menus

Press Mode to access menus.

- Scrolling

○ Scroll music, menus

○ Fast Forward / Reverse when playing music.

- List of Menus

To access different menu functions from main menu.

Main menu: (Hold Mode to access)

Music Mode:                  Recorder Mode:                	Play Mode:

FM Mode:                      Settings:                       E-Documents:

Browsing pictures:                         USB Mode (Connect to PC):

- Volume Adjust

Push VOL to access volume adjust, press Next/Last to increase or decrease volume.

- Switch on/off

Press and hold Play to switch on when the player is off.

Press and hold Play to switch off when the player is on.

- Play & Pause; exit from submenu

On music mode, Press Play to play music.

When playing music, press Play to pause; press and hold to stop playing.

- Start / Stop recording

On recording mode, press Play to stop.

Keys Processing

- Keys Functions Definition

- Play: Power On/Off, Play, Pause, Stop

- MODE (Menu ): Entry main menu or exit from current menu.

- Next: Next, FF, Volume increase

- Last: Previous, Rev, Volume decrease

- USB: USB outlet

- Earphone: Standard earphone outlet

- ON/OFF: Power switch

- Key Processing Definition

Keys processing includes 4 actions: Press, Press and Hold, Push, Hold. If not mentioned, all

actions are Press.

Press: Press a key and valid immediately;

Press and Hold: Press a key and hold it at least 1.2s this action valid only once.

Push: Push a key, and valid when released.

Hold: events occur in such frequency then the key is holding such as Fast Forward and Reverse.

4、Play music

- Simple actions

- Put earphone plug into earphone outlet;

- Press and hold Play to switch the player on, then entry Music Mode and press Play to play

music.

- Select a music:  Last: Previous music;

Next: Next music.

4．For AMV files, video play will apply.

- Equalizer Mode

- When playing music

- Press Mode to entry play submenu;

- Push Next choosing Equalizer Mode;

- Press Mode to entry ‘Equalizer Mode’ submenu.

Select an equalizer:

- Detail of each equalizer (EQ):

Natural,  Rock,  Pop,  Classical,  Soft,  Jazz,  DBB

- Push Next to select an EQ and press Mode to confirm.

- Synchronous Lyric Display

The player supports lyric files with *.LRC suffix, and displays synchronously.

How to use lyric files?

Please make sure the lyric has the same name to the music, For example:

Music file: Journey.mp3       Lyric file: Journey.lrc

- How to know if lyric available?

If lyric matched, a green icon  will be displayed on the left down corner of screen,

  - When marched lyric available：     2.  Press and hold Mode to entry lyric interface;

- Lyric displays                      4.  Press Mode return to music mode.

Voice Recording

Please make sure the battery has enough capacity before making record.

Each fold can save up to 99 voice recording files.

- Recording on “Record mode”

1. .Entry main menu.

2. Push Next scroll to Record mode

3. Push Mode to select Record mod, screen will display as below:

4. Press Play to start recording.

Voice will be recorded in current fold which set through ’Record stop / Main fold’

If displayed “Memory full”, it means mo space to save new record files, please delete other files to

release memory space.

If “Fold full” shown, it means there are 99 record files in this fold. Please choose another one.

The player only responses to Play and A-B when record processing

- Select Record Type

1. When in the interface of ‘Record stop’

2. Press Mode to entry record submenu                  3. Push next scrolling into ‘Record type’

submenu then presses Mode to select it.

| Fine record | wav file，fine quality |
| --- | --- |
| Long-time record | act file, normal quality |
| Fine voice control | wav file, (Recording controlled by voice, pause when mute) |
| Long-time voice control | act file, (Recording controlled by voice, pause when mute) |

4. Press Next to choose appropriate type and press Mode to select it

5. Press Play to start recording.

- Play recorded files

- Entry main menu

- Push Next to choose ‘Play mode’

3.  Push Mode to entry playing interface

4.  Press Play again to play the file.

5.  Choose voice record files:

Last: Select previous file;

Next: Select the next file;

Convert ACT Files into WAV format

The ACT file which produced by this player can be converted into WAV format by using software provided.

1. Imply “Sound Converter” program.                        2. Select the ACT files you would like

Clock “OPEN” button                                       to convert

- Click ‘CONVERT’ button, the program will start converting,

PS: This tool can also play WAV and MP3 files.

Using FM radio

- NOTE: 20 channels can be saved each in “General Frequency” and “Japan Frequency”

1. Entry main menu;

2. Push Next scrolling “FM Mode”

3. Push Mode to entry

4. Auto tuning

Hold Last/Next 2 seconds to start the channel search in 100 KHz interval upwards or downwards.

To stop tuning, push Last/Next.

5. Manual tuning

Push Last: Downward 100 KHz

Push Next: Upward 100 KH

6. Save current channel:

Push Mode to entry FM submenu.

Press Mode again to save channel.

7. Listening to a saved channel:

You can press Play to choose a saved channel.

9. Volume control: Push VOL to access volume adjust, press Next/Last to increase or decrease volume.

Settings

- Entry Settings

You can set system performances here,

options may vary in different firmware version

1. Entry main menu

2. Push Next Scrolling into “Settings”

3. Press Mode to entry.

- Options introduction:

| (Recording Time) | Setting date and time when saving recorded file |
| --- | --- |
| (Screensaver) | Screensaver setting |
| (Language) | Choosing different languages |
| (Timing shut off) | Setting a count down time in minutes, the player will shut off when time out. |
| (Repeat Setting) | Setting repeat status |
| (Contrast Setting) | Setting display’s contrast |
| (PC Mode) | Options for ‘Secret Space’ |

| (Memory Status) | Check memory space and usage status |
| --- | --- |
| (Firmware Ver.) | Version of player’s firmware |
| (Upgrade Firm.) | Use for upgrade firmware |
| (Exit) | Exit from Setting interface |

- List of menus:

○’Recording time’ Setting

    - System setting interface

2.  Press Mode to entry ‘Recording time’ interface recording time:

- Push VOL setting from years. While setting, year on twinkling.

- Push Next the value will increase (Last on opposite)

- After setting, press Mode to exit.

○ “Screensaver” Setting

- Press Mode entry screensaver setting;

- Push Next for choosing  (Last for previous)

- After setting, press Mode to exit.

○ Language Setting

This player have 17 display languages: Simplified Chinese, English, Traditional Chinese,

Japanese, Korean, French, Germany, Italian, Spanish, Portuguese, Dutch, Swedish, Czech,

Danish, Polish, Thai and Russian.

- Press Mode to entry ‘Language’ interface

  - Push Next / Last to scrolling.

  - After setting, press Mode to exit.

○Turning off Setting

Please note:

You can set time in seconds on ‘Battery saving’ mode, allow the player shut down automatically

when player become stop and idle for the period you have set. This function id void if the time set to 0.

You can set time in minutes on ‘Sleep mode’, allow the player shut down automatically when the

player become idle (regardless current status) for the period you have set. It is designed for listening

music before sleep. Please note: Sleep mode valid only once after setting, you have to set again if you

want to use it next time.

○’Repeat Settings’

Please consult into ‘Sound Setting’

Note: in “Manual Mode” you should set repeat point manually.

In “Automatic Mode” the player can identify sentence automatically when on A-B repeat. (This

function is designed for repeat sentences in language studies.)

○’PC connection’ Setting

Please consult into ‘Sound Setting’

Some operation systems (Windows 2K SP4 or prior) may not recognize a USB disk with two

symbols. Therefore, you have to choose an active disk here when using ‘Secret Space’ function only

the active disk can be found in PC.

○’Memory status’

You can check total memory space and the percentage of usage.

○’Firmware version’

You can find the player’s firmware’s version.

○’Firmware upgrade’

Use for upgrade player’s firmware.

Tips: Press Play can exit current menu quickly. The function is valid on all other menus.

Play Videos

1. Entry main menu, press Next scrolling to “MOVIE”(Only available to AMV files):

2. Press MODE to entry:

3. Press PLAY to starting play

- Reading Documents

１.  On main menu, press Next/Last choosing e-Document,

２.  Press Mode to entry corresponding submenu:

３．Press Next or Last choosing the document you want to read,

then press Play to read it.

Note: If you are set in ‘Manual play’ you must scroll text via Next or

Last; texts can be scrolled automatically under ’Auto play’ set.

- Browsing Pictures

This function is only available for JPEG format.

- On main menu, press Next/Last choosing Browsing pictures.

- Press Mode to entry corresponding submenu:

- Press Next or Last choosing the document you want to read,

then press Play to play it..

9.Game

1. Entry main menu;

Russian diamonds

Control direction and speed of the falling diamonds by direction key.

Rotate the diamonds by circumrotate key. Once a line is filled, then it will be clear away, and other diamond above will move downwards. Meanwhile one line clear away, you get 100 mark, 300 mark for two lines, 800 mark for three lines, 1500 mark for four lines. It will speed up each time you got a 10000 mark.

MENU Button:Exit

NEXT Button: Move object brick from right

PREV Button: Move object brick from left

PLAY Button: Switch graph of brick direction

VOL Button：Speedup aim brick speed of whereabouts

10、Using USB Disk

The player is also a standard USB disk. Supported by Windows98 (drivers needed), Windows 2K or above (no need for drivers), Mac OS 10.3, Redhead Linux 8.0 or above.

This player supports USB power supply, it can be used without battery. Press Mode at ‘Waiting Mode’, Can quickly exit to main menu, and you can choose a mode you would like to entry.

This player support suspend mode.

There are three display modes available when connected to ‘pc’.

| 1. Waiting | 2. Downloading |
| --- | --- |
| 3. Uploading |  |

Other settings

- Choose other fold (Stop submenu)

You can classify files into several different folders that ease to manage them (folders should be created

on PC). The player can identify 9 folders in root

| 1. When stopped | 2. Press Mode to entry Stop submenu |
| --- | --- |
| 3. Press Mode to entry folder choosing interface | 4. Press Next or Last to choose a folder |
| 5.Press Mode to entry selected folder. |

Please note: You can set folders independently in Music / Recorder / Play mode

- Delete file (Stop submenu)

You delete correspond files/channels in each Music/Play/FM modes.。

| 1.When Stopped. (No stop interface in FM mode) | 2.Press Mode to entry Stop submenu |
| --- | --- |
| 3.Press Next or Last to choose ‘Delete file’ or ‘Delete all’. | 4. Press Next to choose ‘YES’ |
| 5.Press Mode to confirm delete. |

‘Delete all’ will delete all files in current folder of current mode. I.e. Choose ‘Delete all’ in Music mode

will delete all music files; recorder files will not be affected.

On FM mode, all saved channel will be removed.

Please safely removed player and unplug USB cable after delete files on PC, otherwise some files will

not be removed.

- Play mode (Play submenu)

You can choose different play mode (i.e. repeat, shuffle) when playing music or recorded files.

The first option on Play submenu is ‘Play mode’

○ REPEAT

| (Normal) | Playing music files in sequence until the end of folder |
| --- | --- |
| (Repeat One) | Repeat single music file |
| (Folder) | Play all music files in folder |
| (Repeat Folder) | Repeat all music files in folder |
| (Repeat All) | Repeat all music files |

○SHUFFLE

| (Random) | Play music files in folder randomly |
| --- | --- |

○INTRO

| (Intro) | Play the 10s of each music files in sequence |
| --- | --- |

- Tempo rate(Play submenu)

You can choose different play speed and not affect to sound. (Only valid to MP3 files)

- While playing music

- Push Mode to entry play submenu

- Push Next scrolling to ‘Play speed’ option

- Push Mode to entry

- Push Next for faster, Last for slower

Note: Play speed will applied to all music file

- Repeat mode (Play submenu)

Entry from Play submenu:

○ A-B Repeat

1. When play music or recorder

2. Push Mode to entry play submenu

3. Push Next scrolling into ‘Repeat Mode’ option

4. Push Mode to entry

Repeat Mode: ‘A’ of Symbol flashes, waiting for starter A

5. Push Next to select ‘A’

‘B’ of symbol flashes, waiting ender B

- Push Next to select B. Symbol  fixed and starting repeat between A-B, while playing,

you can push Last to reset A point.

In repeat mode, you can press VOL+ or VOL- to adjust playing speed

○ Karaoke Mode (No such Function in Playing mode)

| 1. A-B repeating | 2.Push Next entry Karaoke mode |
| --- | --- |
| 3. Repeat symbol ’ ’ will be replaced to karaoke symbol ’ ’. Player begins recording voice to the length of A-B repeat period. | 4. Upon time reaches, player resume play music file and the symbol replaced to’ ’, push Next entry contrast function. |

Press Last returns to Repeat A-B status.。

○Contrast Function (No such Function in playing mode)

| 1. While entry contrast function, repeat symbol displayed as“”, the original sound will be played. | 2. While finish original, repeat symbol will be replaced to“”, player will play the voice recorded. |
| --- | --- |

Push Last return to ‘Karaoke mode’

Press Mode to exit repeat mode upon above three modes.

- Repeat times (Play submenu)

Please consult into ‘Backlight time setting’

Repeat time determines the times of play A-b repeat until exit

- Repeat interval (Play submenu)

Please consult into ‘Backlight time setting’

Repeat interval determines the time period between previous repeat (in seconds).

- New Function Recommends!

About Secret Space

Some MP3 user may worry about divulging secret. They do not want others to find private

information contained, therefore these data have to be removed before lend their own MP3 to others. It

makes some trouble.

However, this problem has totally solved by ‘Secret Space’ technique!

You can use provided software to divide the whole USB disk into two parts, and encrypt one of them.

You can move your privacy into the encrypted part; they will be protected by password.

To active ‘Secret Space’:

- Connect your player to PC

- Run MP3 Player Disk Tool which can be found in provided CDROM: (Picture 11-1)

- Click ‘Allocation and Encrypt’ card, Allocate appropriate space and set username and password,

and then click Start.  (Picture 11-2)

(Picture 11-1)                                       (Picture 11-2)

- After space allocation, shown as below: (Picture 11-3)

- Click ‘OK’ to restart.

- After restart you will find two disks (only one disk can be seen on Windows 2K SP4or prior),

click the encrypted disk (the second one), you will find three files, two are hidden, one is executable.

(Picture 11-3)                               (Picture 11-4)

- Running executable file ‘RdiskDecrypt.exe’ and input username and password. If all are correct,

disk will be opened, and files can be copied into.

- You must enter username and password each time access

encrypted disk.

Warning: Divide one disk into parts will remove all data, and

so does combine process.

Warning: Please remember username and password. If you forget it, you can only making

combine processing and you will loss all encrypted data.

## Convert Video files into AMV

This program is used to convert video files into AMV

format, currently only WMV format is supported.

1． Run “AMV Convert Tools”, click  to choose

the folder where to save the AMV files, then click  to

select the folder where the original files are.

(Picture 12-1)

２．Select unprocessed AMV files, then click, the

icon will be highlighted into  and a dialog box will

shown. Choosing Pixels of AMV to “128 * 128” and

Frames per second to “middle”, then click OK to confirm.

(Note: Only pixels in 128*128 can be supported)                        (Picture 12-1)

(Picture 12-2)

３．Click  to start converting. (Picture 12-3)

(Picture 12-2)                                   (Picture 12-3)

4．After convert, the AMV files will be played automatically.

## ●Troubleshooting

| No Power | Check if battery had installed properly Make sure you have switched the player on |
| --- | --- |
| No Sound | Make sure volume is not on 0 position and the connection to earphone is valid Please make sure the earphone is clean Damaged MP3 files may have noise and even cannot be played |
| Strange characters on display | Make sure you have chose correct language |
| FM has bad performance | Adjust place of player and earphone Switch off power appliance nearby Earphone can be used as antenna |
| Cannot Download Music | Check USB cable, and make sure the player is properly connected to the PC Check if the driver has well installed Make there is still blank memory |

Technical Specifications

| Dimension |  |
| --- | --- |
| Weight |  |
| Screen | 18 “ TFT |
| Connecting to PC | High Speed USB2.0 |
| Memory | 128M – 1GB Flash |
| The playing time of battery | In the mode of full screen shown on, it can play in audio or video for max 3.5 hours. In the mode of black screen, It can play in audio for max 8 hours (please choose "black" in LCD SET, then, it play audio without display). |
| Voice Recorder | Sample rate | 8KHz |
|  | Format | WAV (32K bps), ACT (8K bps) |
|  | Time | 35hours (ACT, 128M Flash) |
| MP3、WMA、WMV、ASF | Max. Output | (L) 10mW + (R)10mW (32Ohm) |
|  | MP3 Bit rate | 8K bps – 320K bps |
|  | WMA、WMV、ASF Bit rate | 5K bps – 384K bps |
|  | Freq. Response | 20Hz to 20KHz |
|  | SNR | 85dB |
|  | Distortion |  |
| FM Radio | Freq. Range | 76MHz – 90MHz / 87MHz – 108MHz |
|  | Max. Stored Channels | 20 + 20 |
|  | Max. Output | (L) 10mW + (R)10mW (32Ohm) |
|  | SNR | 45dB |
| Supported Music Formats | MP1, MP2, MP3, WMA, WMV, ASF, WAV |
| Operate Temperature | -5 to 40 degree |
| 17 Languages Display | Simp Chinese, English, Trad Chinese, Japanese, Korean, Itanlan etc. |
| Supported Systems | Windows98/SE/ME/2K/XP、Mac OS 10、Linux 2.4.2 |

Please note: Design and characters may change without prior notice.